## Slide 1: Direct Memory Access Controller
Module 8
C2000™ Microcontroller Workshop
Copyright © 2015 Texas Instruments. All rights reserved.

## Slide 2: Module Objectives
Understand the operation of the Direct Memory Access (DMA) controller
Show how to use the DMA to transfer data between peripherals and/or memory without intervention from the CPU

## Slide 3: DMA Triggers, Sources, and Destinations
McBSP
DMA
6-channels
ADC
Result 0-15
Triggers
PIE
DINTCH1-6
PWM1
PWM2
PWM11
PWM12
GS0 RAM
GS15 RAM
EMIF
ADCA/B/C/D (1-4, EVT)
MXEVTA/B MREVTA/B
XINT1-5 TINT0-2
ePWM1-12 (SOCA-B)
SD1FLT1-4 SD2FLT1-4
SPITX/RX (A-C)
USBA_EPx_RX/TX1-3
software
IPC RAM
SPI

## Slide 4: DMA / CLA Common Peripheral Access
Common peripherals can be accessed by the CPU and either DMA or CLA
CLA Access | DMA Access
ePWM/HRPWM, eCAP, eQEP, CMPSS, DAC, SDFM | ePWM/HRPWM, SDFM
SPI A/B/C, McBSP A/B, uPP | SPI A/B/C, McBSP A/B
PF1
PF2
1 - 0
3 - 2
15 - 4
PF2SEL
PF1SEL
reserved
CpuSysRegs.SECMSEL
x0 = connected to CLA *
x1 = connected to DMA
* Default (lock bit protected)
Note: CPUSELx bit associated with each peripheral defines if the peripheral is connected to CPU1 or CPU2
CPUx
CPUx.CLA
CPUx.DMA
Arbiter
CPUx Peripheral Frame 1
CPUx.SECMSEL
CPUx Peripheral Frame 2

## Slide 5: DMA Definitions
Word
  16 or 32 bits
  Word size is configurable per DMA channel
Burst
  Consists of multiple words
  Smallest amount of data transferred at one time
Burst Size
  Number of words per burst
  Specified by BURST_SIZE register
    5-bit ‘N-1’ value (maximum of 32 words/burst)
Transfer
  Consists of multiple bursts
Transfer Size
  Number of bursts per transfer
  Specified by TRANSFER_SIZE register
    16-bit ‘N-1’ value - exceeds any practical requirements

## Slide 6: Simplified State Machine Operation
Burst Size times
Transfer Size times
The DMA state machine at its most basic level is two nested loops
End Transfer
Move Word
Start Transfer
DMA can be configured to re-initialize at the end of the transfer (continuous mode)

## Slide 7: Basic Address Control Registers
SRC_ADDR
SRC_ADDR_SHADOW
DST_ADDR
DST_ADDR_SHADOW
SRC_BURST_STEP
SRC_TRANSFER_STEP
DST_BURST_STEP
DST_TRANSFER_STEP
Active pointers
Pointer shadow registers copied to active pointers at start of transfer
Signed value added to active pointer after each word
Signed value added to active pointer after each burst
32

## Slide 8: Simplified State Machine Example
3 words/burst
2 bursts/transfer
Read/Write Data
Add Burst Step
to Address
Pointer
Add Transfer
Step to Address
Pointer
Moved
“Burst Size”
Words?
Moved
“Transfer Size”
Bursts?
Y
Y
N
N
Wait for event
to start/continue
transfer
Start Transfer
End Transfer

## Slide 9: DMA Interrupts
Each DMA channel has its own PIE interrupt
The mode for each interrupt can be configured individually
The CHINTMODE bit in the MODE register selects the interrupt mode
Read/Write Data
Add Burst Step
to Address
Pointer
End Transfer
Add Transfer
Step to Address
Pointer
Moved
“Burst Size”
Words?
Moved
“Transfer Size”
Bursts?
Y
Y
N
N
Wait for event
to start/continue
transfer
Start Transfer
Mode #1: Interrupt at start of transfer
Mode #2: Interrupt at end of transfer
Notes: 两种中断的应用背景是什么

## Slide 10: Simple Example
0x4444
0x0000
0x00004003
0x00004002
0x00004001
0x00004000
0x00000000
0x0000F003
0x0000F002
0x0000F001
0x0000F000
0x00000000
0x3333
0x0000
0x2222
0x0000
0x0000F000
0x1111
0x0000
Read/Write Data
Add Burst Step
to Address
Pointer
End Transfer
Add Transfer
Step to Address
Pointer
Moved
“Burst Size”
Words?
Moved
“Transfer Size”
Bursts?
Y
Y
N
N
Wait for event
to start/continue
transfer
SRC_ADDR_SHADOW
SRC_ADDR
SRC_BURST_STEP
SRC_TRANSFER_STEP
BURST_SIZE*
TRANSFER_SIZE*
Addr
Value
0x1111
0xF000
0x2222
0xF001
0x3333
0xF002
0x4444
0xF003
Source Registers
0x0001
0x0001
0x0001
0x0001
DST_ADDR_SHADOW
DST_ADDR
DST_BURST_STEP
DST_TRANSFER_STEP
Addr
Value
0x4000
0x4001
0x4002
0x4003
Destination Registers
0x00004000
0x0001
0x0001
2 words/burst
2 bursts/transfer
* Size registers are N-1
Objective: Move 4 words from memory location 0xF000 to memory location 0x4000 and interrupt CPU at end of transfer
Start Transfer
Note: This example could also have been done using 1 word/burst and 4 bursts/transfer, or 4 words/burst and 1 burst/transfer. This would affect Round-Robin progression, but not interrupts.
Interrupt to PIE

## Slide 11: Data Binning Example
ADCA Results
GS3 RAM
CH0
CH1
CH2
CH3
CH4
0x0B00
CH0
CH1
CH2
CH3
CH4
CH0
CH1
CH2
CH3
CH4
1st Conversion Sequence
0xF000
0xF003
0xF006
0xF009
0xF00C
0x0B01
0x0B02
0x0B03
0x0B04
0xF001
0xF004
0xF007
0xF00A
0xF00D
0xF002
0xF005
0xF008
0xF00B
0xF00E
2nd Conversion Sequence
3rd Conversion Sequence
CH0
CH1
CH2
CH3
CH4
Objective: Bin 3 samples of 5 ADC channels, then interrupt the CPU

## Slide 12: Data Binning Example Register Setup
* Size registers are N-1
BURST_SIZE*
TRANSFER_SIZE*
0x0004
5 words/burst
0x0002
3 bursts/transfer
SRC_ADDR_SHADOW
SRC_BURST_STEP
SRC_TRANSFER_STEP
0x00000B00
0x0001
DST_ADDR_SHADOW
DST_BURST_STEP
DST_TRANSFER_STEP
0x0003
0xFFF5
(-11)
0xFFFC
(-4)
CH4
CH3
CH2
CH1
CH0
0x0B00
0x0B01
0x0B02
ADCA Results
GS3 RAM
0xF000
0xF003
0xF006
0xF009
0xF00C
CH0
CH0
CH0
CH1
CH1
CH1
CH2
CH2
CH2
CH3
CH3
CH3
CH4
CH4
CH4
0xF001
0xF004
0xF007
0xF00A
0xF00D
0xF002
0xF005
0xF008
0xF00B
0xF00E
0x0B03
0x0B04
Objective: Bin 3 samples of 5 ADC channels, then interrupt the CPU
SOC0 – SOC4 configured to CH0 – CH4, respectively, ADCA configured to re-trigger (continuous conversion)
ADC Registers:
DMA Registers:
0x0000F000
starting address**
** Typically use a relocatable symbol in your code, not a hard value

## Slide 13: Ping-Pong Buffer Example
ADCA Result Register
50 word ‘Ping’ buffer
50 word ‘Pong’ buffer
GS0 RAM
0x0B00
DMA Interrupt
DMA Interrupt
0xC140
Objective: Buffer ADC ch. 0 ping-pong style, 50 samples per buffer
ADCRESULT0
SOC0 configured to ADCINA0 with 1 conversion per trigger

## Slide 14: Ping-Pong Example Register Setup
DMA configured to re-init after transfer (CONTINUOUS = 1)
SRC_BURST_STEP
SRC_TRANSFER_STEP
0x0000
DST_BURST_STEP
DST_TRANSFER_STEP
0x0001
SRC_ADDR_SHADOW
DST_ADDR_SHADOW
BURST_SIZE*
TRANSFER_SIZE*
0x0000
1 word/burst
0x0031
50 bursts/transfer
* Size registers are N-1
Objective: Buffer ADC ch. 0 ping-pong style, 50 samples per buffer
don’t care
since BURST_SIZE = 0
don’t care
since BURST_SIZE = 0
0x00000B00
starting address
0x0000C140
starting address**
Read/Write Data
Add Burst Step
to Address
Pointer
End Transfer
Add Transfer Step
to Address Pointer
Moved
“Burst Size”
Words?
Moved
“Transfer Size”
Bursts?
Y
Y
N
N
Wait for event to
start/continue transfer
Start Transfer
Convert ADCA Channel ADCINA0 – 1 conversion per trigger (i.e. ePWM2SOCA)
DMA Registers:
ADC Registers:
Other:
** DST_ADDR_SHADOW must be changed between ping and pong buffer address in the DMA ISR. Typically use a relocatable symbol in your code, not a hard value.

## Slide 15: Channel Priority Modes
Round Robin Mode:
  All channels have equal priority
  After each enabled channel has transferred a burst of words, the next enabled channel is serviced in round robin fashion
Channel 1 High Priority Mode:
  Same as Round Robin except CH1 can interrupt DMA state machine
  If CH1 trigger occurs, the current word (not the complete burst) on any other channel is completed and execution is halted
  CH1 is serviced for complete burst
  When completed, execution returns to previous active channel
  This mode is intended primarily for the ADC, but can be used by any DMA event configured to trigger CH1
DMA
event?
CH6
CH1
CH2
CH5
CH4
CH3
Y
N

## Slide 16: Priority Modes and the State Machine
Read/Write Data
Add Burst Step
to Address
Pointer
Add Transfer
Step to Address
Pointer
Moved
“Burst Size”
Words?
Moved
“Transfer Size”
Bursts?
Y
Y
N
N
Point where other
pending channels
are serviced
Wait for event
to start/continue
transfer
Point where
CH1 can
interrupt other
channels in
CH1 Priority Mode
Start Transfer
End Transfer

## Slide 17: DMA Throughput
4 cycles/word (5 for McBSP reads)
1 cycle delay to start each burst
1 cycle delay returning from CH1 high priority interrupt
32-bit transfer doubles throughput (except McBSP, which supports 16-bit transfers only)
  Example: 128 16-bit words from ADC to RAM
    8 bursts * [(4 cycles/word * 16 words/burst) + 1] = 520 cycles
  Example: 64 32-bit words from ADC to RAM
    8 bursts * [(4 cycles/word * 8 words/burst) + 1] = 264 cycles

## Slide 18: DMA vs. CPU Access Arbitration
DMA has priority over CPU
  If a multi-cycle CPU access is already in progress, DMA stalls until current CPU access finishes
  The DMA will interrupt back-to-back CPU accesses
Can the CPU be locked out?
  Generally No!
  DMA is multi-cycle transfer; CPU will sneak in an access when the DMA is accessing the other end of the transfer (e.g. while DMA accesses destination location, the CPU can access the source location)

## Slide 19: DMA Registers DmaRegs.name (lab file: Dma.c)
DMACTRL DMA Control Register
PRIORITYCTRL1 Priority Control Register 1
MODE Mode Register
CONTROL Control Register
BURST_SIZE Burst Size Register
BURST_COUNT Burst Count Register
SRC_BURST_STEP Source Burst Step Size Register
DST_BURST_STEP Destination Burst Step Size Register
TRANSFER_SIZE Transfer Size Register
TRANSFER_COUNT Transfer Count Register
SRC_TRANSFER_STEP Source Transfer Step Size Register
DST_TRANSFER_STEP Destination Transfer Step Size Register
SRC_ADDR_SHADOW Shadow Source Address Pointer Register
SRC_ADDR Active Source Address Pointer Register
DST_ADDR_SHADOW Shadow Destination Address Pointer Register
DST_ADDR Active Destination Address Pointer Register
DMACHSRCSELx (x = 1 or 2) Trigger Source Selection Register
Register Description
DMA CHx Registers
Refer to the Technical Reference Manual for a complete listing of registers

## Slide 20: DMA Control Register DmaRegs.DMACTRL
HARDRESET
PRIORITYRESET
0
15 - 2
reserved
1
Priority Reset
0 = writes ignored (always reads back 0)
1 = reset state-machine after any pending
burst transfer complete
Hard Reset
0 = writes ignored (always reads back 0)
1 = reset DMA module

## Slide 21: Priority Control Register 1 DmaRegs.PRIORITYCTRL1
CH1PRIORITY
0
15 - 1
reserved
DMA CH1 Priority
0 = same priority as other channels
1 = highest priority channel

## Slide 22: Mode Register DmaRegs.CHx.MODE
15
11
10
CONTINUOUS
ONESHOT
13 - 12
14
Channel Interrupt
0 = disable
1 = enable
Data Size Mode
0 = 16-bit transfer
1 = 32-bit transfer
Continuous Mode
0 = DMA stops
1 = DMA re-initializes
One Shot Mode
0 = one burst transfer per trigger
1 = subsequent burst transfers occur without additional trigger
CHINTE
DATASIZE
reserved
9
4 - 0
6 - 5
7
8
Channel Interrupt Generation
0 = at beginning of transfer
1 = at end of transfer
Peripheral Interrupt Trigger
0 = disable
1 = enable
CHINTMODE
PERINTE
OVRINTE
PERINTSEL
reserved
Overflow Interrupt Enable
0 = disable
1 = enable
Peripheral Interrupt Source Select
Set bits to the channel number
See Trigger Sources on next slide

## Slide 23: DMA Trigger Source Selection Registers
Selects the Trigger Source for each DMA channel
  Each channel can be triggered by up to 256 interrupt sources
  Select ‘no peripheral’ if trigger is generated by software
  Default value = 0x00
  See “Peripheral Interrupt Trigger Sources” table on next slide
CH4
31 - 24
7 - 0
CH3
CH2
CH1
23 - 16
15 - 8
DmaClaSrcSelRegs.DMACHSRCSEL1
reserved
31 - 24
7 - 0
reserved
CH6
CH5
23 - 16
15 - 8
DmaClaSrcSelRegs.DMACHSRCSEL2
Note: DMACHSRCSELLOCK register can be used to lock above registers (lock bit for each register)

## Slide 24: Peripheral Interrupt Trigger Sources
0 | No Peripheral | 13 | ADCCINT3 | 36 | EPWM1SOCA | 49 | EPWM7SOCB | 70 | TINT2 | 109 | SPITXDMAA
1 | ADCAINT1 | 14 | ADCCINT4 | 37 | EPWM1SOCB | 50 | EPWM8SOCA | 71 | MXEVTA | 110 | SPIRXDMAA
2 | ADCAINT2 | 15 | ADCCEVT | 38 | EPWM2SOCA | 51 | EPWM8SOCB | 72 | MREVTA | 111 | SPITXDMAB
3 | ADCAINT3 | 16 | ADCDINT1 | 39 | EPWM2SOCB | 52 | EPWM9SOCA | 73 | MXEVTB | 112 | SPIRXDMAB
4 | ADCAINT4 | 17 | ADCDINT2 | 40 | EPWM3SOCA | 53 | EPWM9SOCB | 74 | MREVTB | 113 | SPITXDMAC
5 | ADCAEVT | 18 | ADCDINT3 | 41 | EPWM3SOCB | 54 | EPWM10SOCA | 95 | SD1FLT1 | 114 | SPIRXDMAC
6 | ADCBINT1 | 19 | ADCDINT4 | 42 | EPWM4SOCA | 55 | EPWM10SOCB | 96 | SD1FLT2 | 131 | USBA_EPx_RX1
7 | ADCBINT2 | 20 | ADCDEVT | 43 | EPWM4SOCB | 56 | EPWM11SOCA | 97 | SD1FLT3 | 132 | USBA_EPx_TX1
8 | ADCBINT3 | 29 | XINT1 | 44 | EPWM5SOCA | 57 | EPWM11SOCB | 98 | SD1FLT4 | 133 | USBA_EPx_RX2
9 | ADCBINT4 | 30 | XINT2 | 45 | EPWM5SOCB | 58 | EPWM12SOCA | 99 | SD2FLT1 | 134 | USBA_EPx_TX2
10 | ADCBEVT | 31 | XINT3 | 46 | EPWM6SOCA | 59 | EPWM12SOCB | 100 | SD2FLT2 | 135 | USBA_EPx_RX3
11 | ADCCINT1 | 32 | XINT4 | 47 | EPWM6SOCB | 68 | TINT0 | 101 | SD2FLT3 | 136 | USBA_EPx_TX3
12 | ADCCINT2 | 33 | XINT5 | 48 | EPWM7SOCA | 69 | TINT1 | 102 | SD2FLT4 |  | 
// Set DMA Channel 2 to trigger on EPWM1SOCA
DmaClaSrcSelRegs.DMACHSRCSEL1.bit.CH2 = 36;
Note: values not shown in table are reserved

## Slide 25: Control Register DmaRegs.CHx.CONTROL
reserved
OVRFLG
15
11
8
10 - 9
RUNSTS
BURSTSTS
TRANSFERRST
12
13
14
Overflow Flag *
0 = no overflow
1 = overflow
Run Status *
0 = channel disabled
1 = channel enabled
Burst Status *
0 = no activity
1 = servicing burst
Transfer Status *
0 = no activity
1 = transferring
Peripheral Interrupt Trigger Flag *
0 = no interrupt event trigger
1 = interrupt event trigger
* = read-only
PERINTFLG
reserved
7
3
0
2
PERINTCLR
PERINTFRC
SOFTRESET
HALT
RUN
1
4
6 - 5
Error Clear
0 = no effect
1 = clear SYNCERR
Peripheral Interrupt Clear
0 = no effect
1 = clears event and PERINTFLG
Peripheral Interrupt Force
0 = no effect
1 = sets event and PERINTFLG
Soft Reset
0 = no effect
1 = default state
Halt
0 = no effect
1 = halt
Run
0 = no effect
1 = run
ERRCLR
reserved

## Slide 26: Lab 8: Servicing the ADC with DMA
ADC
RESULT0
ePWM2
connector
wire
ADCINA0
data
memory
Pointer
rewind
Display using CCS
TB Counter
Compare
Action Qualifier
ePWM1
ePWM2 triggering ADC on period match using SOCA trigger every 20 µs (50 kHz)
Objective:
Configure the DMA to buffer ADCA Channel A0 ping-pong style with 50 samples per buffer
ping
CPU writes data to AdcBuf during DMA ISR
pong
data
memory
DMA

## Slide 27
C2000 Technical Training
www.ti.com/c2000